## Slide 1
ELE 573 · BRAIN SIGNAL PROCESSING
SPRING 2026
Alpha Wave
Detection via
Tripolar Rings.
A signal-processing pipeline comparing tEEG against conventional EEG across a six-subject cohort.
Shayan Khodabakhsh · University of Rhode Island

## Slide 2
02 · METHODS
Setup, signals, and metrics.
THE SIGNALS
TCRE = three concentric rings on one sensor. The geometry computes the surface Laplacian directly at the scalp.
tEEG (odd channels) = local cortical activity via Laplacian.
eEEG (even channels) = volume-conducted, like a normal disc electrode.
THE SETUP
11 channels recorded simultaneously over occipital cortex:
F1
Ch1 / Ch2
FELT
F2
Ch3 / Ch4
FELT
F3
Ch5 / Ch6
FELT
F4
Ch7 / Ch8
FELT
P5
Ch9 / Ch10
PASTE
D
Ch11
DISC
Protocol: 7 alternating eyes-open/closed epochs + 3 visual-stimulation blocks.
FOUR METRICS
I
Alpha SNR & reactivity
Closed/open ratio.
II
FOOOF decomposition
1/f vs. peaks.
III
Spectrogram SSIM
Image-similarity.
IV
VEP & disc correlation
Per-channel agreement.
TOOLS Python · MNE · FOOOF (specparam) · SciPy · scikit-image
Khodabakhsh · ELE 573 · Spring 2026
02 / 13

## Slide 3
03 · COHORT
6
subjects
Same protocol.
Same metrics.
One emerging pattern.
Subject | QC | α SNR (dB) | Reactivity | Paste r vs disc | Paste SSIM | Felt SSIM
SK1 | POOR | — | <1.0× | — | 0.40 | —
HS | POOR | 1.8 | 1.27× | 0.93–0.94 | 0.72 | 0.24–0.37
RK | POOR | 1.8 | 0.99× | 0.95–0.96 | 0.78 | 0.18–0.31
SG | POOR | 1.6 | 1.39× | 0.80–0.81 | 0.60 | 0.12–0.27
TU2 | MIXED | 2.6 | 2.63× | 0.99+ | 0.66 | 0.27–0.34
LS2 | POOR | 2.9 | 1.81× | 0.98+ | 0.79 | 0.28–0.34
Khodabakhsh · ELE 573 · Spring 2026
03 / 13

## Slide 4
04 · FINDINGS
FELT · TCRE #2
SSIM 0.27 · LOW agreement
PASTE · TCRE #5
SSIM 0.66 · HIGH agreement
Khodabakhsh · ELE 573 · Spring 2026
04 / 13

## Slide 5
05 · WHERE ALPHA LIVES
TU2 · Ch9 (Paste tEEG). Bright stripes at 8–13 Hz fire during every Closed block, vanish during Open.
Khodabakhsh · ELE 573 · Spring 2026
05 / 13

## Slide 6
06 · SPECTRA BY SENSOR
Where the alpha peak shows up.
TU2 · PSD per channel after 60 Hz notch.
CH9, CH10, CH11
Paste channels show a sharp, well-localized peak at the canonical alpha frequency.
CH5, CH7
Felt tEEG occasionally shows a peak (≈11 Hz), but the shape is broader and lower-amplitude.
CH1–CH4, CH6, CH8
No reliable alpha peak. Mostly 1/f decay or broad noise floor.
Khodabakhsh · ELE 573 · Spring 2026
06 / 13

## Slide 7
07 · FOOOF DECOMPOSITION
CH9 — PASTE TEEG
R² = 0.985
CH10 — PASTE EEEG
R² = 0.959
CH11 — PASTE DISC
R² = 0.958
Real alpha, not 1/f bias. FOOOF separates the aperiodic 1/f component (gray) from the periodic alpha peak (red). All three paste channels fit at R² > 0.95.
Khodabakhsh · ELE 573 · Spring 2026
07 / 13

## Slide 8
08 · OPEN VS. CLOSED
Berger, in the spectrum.
TU2 · eyes-open (green) vs. eyes-closed (blue) PSDs.
Ch9 / Ch10 / Ch11
Closed visibly higher than open at 10–12 Hz. Clean Berger signature.
Ch5, Ch7 (felt tEEG)
Modest closed > open at alpha. Berger is detectable but partial.
Ch1, Ch3 (felt tEEG)
Curves overlap completely. Clipping floods both states with broadband power.
Ch4, Ch8 (felt eEEG)
Closed sometimes lower than open — opposite of Berger. Not interpretable.
Khodabakhsh · ELE 573 · Spring 2026
08 / 13

## Slide 9
09 · TU2 IN FOUR METRICS
The cleanest run, end to end.
Across all four metrics, paste channels (Ch9, Ch10) and the disc reference (Ch11) sit at the right end of every panel.
Α SNR
Felt tEEG sits at 1–3 dB. Paste tEEG hits 6 dB.
REACTIVITY
Paste/disc reach 7–8× closed/open. Felt rarely passes 1×.
DISC R
Paste at r ≈ 1.0. Felt averages near 0.
Khodabakhsh · ELE 573 · Spring 2026
09 / 13

## Slide 10
10 · ACROSS THE COHORT (1 OF 2)
Same paste sensor, every subject.
Ch9 (Paste tEEG). Bright stripes at 8–13 Hz appear during eyes-closed blocks. HS, RK, and SG.
HS
RK
SG
Khodabakhsh · ELE 573 · Spring 2026
10 / 13

## Slide 11
11 · ACROSS THE COHORT (2 OF 2)
Same paste sensor, every subject.
Ch9 (Paste tEEG). TU2 and LS2 — the cleanest two recordings of the cohort.
TU2
LS2
Khodabakhsh · ELE 573 · Spring 2026
11 / 13

## Slide 12
12 · LIMITATIONS
Caveats for interpretation.
HIGH IMPEDANCE ON FELT CHANNELS
Observed. Felt tEEG saturated the ADC at ±3,276.7 µV in 5 of 6 subjects (worst: SG Ch1 ~34%, LS2 Ch1 ~22%, HS Ch3 ~10%).
Implication. Felt SSIM and SNR cannot be cleanly attributed to Laplacian filtering — clipping artifact contributes to the structural disagreement.
VISUAL STIMULATION OVERLAP WITH EYES-OPEN
Observed. Stimulation blocks fall within eyes-open epochs, inflating broadband power during open periods.
Implication. Reactivity ratios computed on raw epochs underestimate the Berger effect. Rest-only analysis recovers the expected pattern (TU2 ≈ 2.6×).
COHORT SIZE AND STATISTICAL INFERENCE
Observed. Six subjects; no formal hypothesis test was performed.
Implication. All cross-subject claims are observational. Pattern consistency supports the conclusion qualitatively, not statistically.
Khodabakhsh · ELE 573 · Spring 2026
12 / 13

## Slide 13
13 · CONCLUSIONS
4
findings
What we built.
What we found.
I
The pipeline is reproducible.
Four metrics applied uniformly to six subjects, eleven channels each.
II
Paste TCRE matches the disc.
Pearson r = 0.93–0.99; spectrogram SSIM 0.60–0.79; FOOOF R² > 0.95 across paste channels.
III
The Berger effect is robust on paste.
Closed/open reactivity up to 8×, visible in single-channel spectrograms across all 5 subjects.
IV
Felt assessment is impedance-limited.
Clipping in 5 of 6 subjects prevents attributing felt SSIM to Laplacian filtering alone.
Thank you.
Shayan Khodabakhsh · University of Rhode Island